## Slide 1
Transportation System
(CV705T)
Prof. Yogesh S. Lanjewar
Assistant Professor
St. VINCENT PALLOTTI COLLEGE OF ENGINEERING &
TECHNOLOGY,NAGPUR
DEPARTMENT OF CIVIL ENGINEERING
UNIT I

## Slide 2
Transportation engineering
Transportation engineering is the
application of scientific technology and
principles to the planning, functional design, operation and management of facilities for any mode of transportation in order to provide for the safe, efficient, rapid, comfortable, convenient, economical, and environmentally compatible movement of people and goods from one place to other.
2

## Slide 3
MODES OF TRANSPORTATION
Basic mode of transportation are
Land
  Roadway
  Railway
Water
Air
3

## Slide 4
MODES OF TRANSPORTATION
Highways
Car, Bus, Truck, non- motorized ..etc
Railways
Trains.
Airways
Aircraft and Helicopters
Waterways
Ships, boats…
4

## Slide 5
Airways
Fastest among all other modes
More comfortable
Time saving
Uneconomical
Waterways
slowest among all other modes
This can be possible between ports on the sea
routes or along the river
economical
5

## Slide 6
Railways
The transportation along the railways track could be advantageous by railways between the stations both for the passengers and goods, particularly for long distance.
It depends upon the road transport
Safety
Economical
6

## Slide 7
Highways
It gives the maximum service to one and all
It gives maximum flexibility for travel with reference to route, direction, time and speed of travel
It provide door to door service
It requires small investment for the government
Motor vehicles are cheaper than other carriers like rail locomotive and wagons
It saves the time for short distance
High degree of accident due to flexibility of movement
7

## Slide 8
Scope of highway engineering
Planning and location
Highway design, geometric and structure
Traffic performance and its control
Materials, construction and maintenance
Economic, finance and administration
8

## Slide 9
Characteristics of road transport
Roads are used by various types of road vehicles, like passenger cars, buses, trucks, pedal cycle and animal drawn vehicle.
It requires a relatively small investment for the
government.
It offers a complete freedom to road users to transfer the vehicle from one lane to another and from one road to another according to need and convenience.
Speed and movement is directly related to the
accident.
9

## Slide 10
HISTORICAL DEVELOPMENT OF ROAD CONSTRUCTION
Oldest mode
  Foot paths- animal ways, cart path……..
As civilization evolved the need for transportation increased
ROMAN ROAD
They were built straight regardless of gradient
They were built after the soft soil was removed and a hard stratum was reached.
Thickness varies from 0.75 m to 1.2m
10

## Slide 11
Roman Road Construction Basic cross section
11

## Slide 12
Modern Highway
Roman Roads
12

## Slide 13
13

## Slide 14
14

## Slide 15
15

## Slide 16
16

## Slide 17
MACADAM CONSTRUCTION

## Slide 18
MACADAM CONSTRUCTION

## Slide 19
19

## Slide 20
20
Mechadam Road

## Slide 21
21

## Slide 22
22

## Slide 23
Indian Roads
India has a large road network of over 3.314 million kilometers of roadways making it 3rd largest road network in the world.
National Highways - 70,548 Km
State Highways - 1,31,899 Km
Major District Roads - 4,67,763 Km
Rural Roads - 26,50,000 Km
23

## Slide 24
Highway Development in India
Jayakar Committee (1927)
Central Road Fund (1929)
Indian Roads Congress (IRC), 1934
Central Road Research Institute (CRRI), 1950
Motor vehicle act (1936)
National Highway Authority of India (NHAI),1995
First twenty year road plan ( 1943-61 )
Second twenty year road plan ( 1961-81 )
Third twenty year road plan ( 1981-2001 )
24

## Slide 25
Jayakar Committee,1927
After the first World War, motor vehicle using the roads increases, this demanded a better road network.
In 1927,Indian road development committee was appointed
by the government with M.R. Jaykar as chairman.
Road development in the country should be made as a national interest since local govt. do not have financial and technical capacity for road development.
An extra tax should be on petrol from road users to
create the road development fund.
To create a national level institution to carry research , development works and consultation.
25

## Slide 26
Central road fund
It was formed on 1st march 1929
The consumers of petrol were charged an extra 2.64 paisa per litre of petrol to built up this road development fund.
From this 20% of annual reveneu is to be retain as a central reveneu for research and experimental work expenses. etc
Balance 80% is allowed by central govt. to various states based on actual petrol consumption
26

## Slide 27
Central Road Fund , 1929
Distribution of 100% on petrol as follows:
57.5% for NH
30% for SH
12.5% for safety works on rail-Road crossing.
50% on diesel for Rural Road development
27

## Slide 28
Indian Roads Congress, 1934
Central semi official body known as IRC was formed in 1934.
To provide ideas related to construction and maintenance of highways.
It is a active body controlling the specification, standardization and recommendations on materials, design of roads and bridges.
It publishes journals, research publications and standard specifications guide lines.
28

## Slide 29
Motor vehicle act
It was formed in 1939
To regulate the road traffic in the form of
traffic laws, ordinances and regulations.
Three phases primarily covered are control of driver, vehicle ownership and vehicle operation
It was revised on 1988
29

## Slide 30
Central road research institute(1950)
engaged in carrying out
projects.
design, construction and
research and development
maintenance of roads
runways, traffic and transportation planning of mega and medium cities, management of roads in different slopes,
Utilization of industrial waste in road construction.
Landslide control.
Ground improvements, environmental pollution.
Road traffic safety.
30

## Slide 31
Based on the Traffic
Heavy
Medium
Light
Based on location and function ( Nagpur road plan )
National highway (NH)
State highway (SH)
Major district road (MDR)
Other district road (ODR)
Village road (VR)
Classification of Highways
31

## Slide 32
Based on modified system of Highways classification
Primary
  Expressways
  National Highways
Secondary
  State Highway
  Major District Road
Tertiary
  Other District Road
  Village Road
32

## Slide 33
Expressways
Heavy traffic at high speed (120km/hrs)
Connects major points of traffic generation
No slow moving traffic allowed
No loading,
The Mumbai-Pune Expressway as seen from Khandala
33

## Slide 34
National Highways
NH are the main highways running through the length and breadth of India, connecting major parts, capital of large states and large industrial and tourist centers.
The national highways have a total length of 70,548 kms. Indian highways cover 2% of the total road network of India and carry 40% of the total traffic.
The highway connecting Delhi-Ambala-Amritsar is denoted as NH---, whereas a bifurcation of this highway beyond Jalandar to Srinagar is denoted NH----A
The longest highway in India is NH--- which stretches from Varansi in Uttar Pradesh to Kanyakumari.
34

## Slide 35
National Highways cont…
ms) connecting Delhi-
)
The shortest highway is NH47A which stretches from Ernakulam to Kochi and covers total length of 4 Kms.
Golden Quadrilateral – (5,846 K
Kolkata-Chennai-Mumbai
  NH-2 Delhi- Kol (1453 km)
 NH 4,7 Che-Mum (1290km)
 NH5&6 Kol- Che (1684 Km)
  NH 8 Del- Mum (1419 km)
35

## Slide 36
State Highways
They are the roads of a state, connecting up with the national highways of adjacent states, district head quarters and important cities within the state.
Total length of all SH in the country is
1,37,119 Kms.
Speed 80 kmph
36

## Slide 37
Major District Roads
Important roads with in a district serving areas of production and markets , connecting those with each other or with the major highways.
India has a total of 4,70,000 kms of MDR.
Speed 60-80kmph
37

## Slide 38
Other district roads
serving rural areas of production
centers
and providing
or other
They are roads connecting villages or group of villages with each other or to the nearest road of a higher category like ODR or MDR.
ODR+VR out of the total 33,15,231 kms of all type of roads.
Speed-40-50 kmph
them with outlet to market important roads like MDR or SH.
Speed 50-60kmph
Village roads
38

## Slide 39
First 20-years road plan(1943-63)
The conference of chief engineer held at Nagpur in 1943 finalized the first 20-years road development plan for India called Nagpur road plan
Road network was classified into five categories.
The responsibility of construction maintenance of NH was assign to central govt.
The target road length was 5,32,700 km at the end of 1961.
39

## Slide 40
First 20-years road plan cont…
The formulae were based on star and grid pattern of road network.
An allowance of 15% is provided for agricultural and industrial development during the next 20-years
The length of railway track in the area was also consider in deciding the length of first category road. The length or railway track is directly subtracted from the estimated road.
40

## Slide 41
Second 20-years road plan(1961-81)
It was initiated by the IRC and was finalised in 1959 at the meeting of chief engineers.
It is known as the Bombay road plan.
The target road length was almost double that of Nagpur road plan i.e. 10,57,330 km.
41

## Slide 42
Second 20-years road plan cont…
the maximum distance from any place in a semi develop area would be 4.8 Km from any road
Expressways have also been considered in this plan and 1600 km of length has been included in the proposed target NH
Length of railway track is considered
independent of road system
5% are to be provided for future development.
42

## Slide 43
Third twenty years road plan (1981-2001)
The future road development should be based on the revised classification of roads system i.e. primary, secondary and tertiary
Develop the rural economy and small towns with all essential features.
Population over 500 should be connected by all roads.
43

## Slide 44
Third twenty years road plan
cont…
Expressway should be constructed along major traffic consideration.
All towns and villages with population over 1500 should be connected by MDR and villages with population 1000-1500 by ODR.
Road should be built in less industrialized areas to attract the growth of industries
The existing roads should be improved by rectifying the defects in the road geometry, widening, riding quality and strengthening the existing pavement to save vehicle operation cost and thus to conserve energy
44

## Slide 45
Highway alignment and surveys
45

## Slide 46
Highway alignment
The position or lay out of centre line of the highway on the ground is called the alignment.
It includes straight path, horizontal deviation and
curves.
Due to improper alignment , the disadvantages are,
  Increase in construction
  Increase in maintenance cost
  Increase in vehicle operation cost
  Increase in accident cost
Once the road is aligned and constructed, it is not easy to change the alignment due to increase in cost of adjoining land and construction of costly structure.
46

## Slide 47
47

## Slide 48
48

## Slide 49
49

## Slide 50
Short
Easy
Safe
Economical
Short- desirable to have a short alignment between two
terminal stations.
Easy- easy to construct and maintain the road with minimum problem also easy for operation of vehicle.
Safe- safe enough for construction and maintenance from the view point of stability of natural hill slope, embankment and cut slope also safe for traffic operation.
Economical- total cost including initial cost, maintenance cost and vehicle operation cost should be minimum.
Requrements of highway alignment
50

## Slide 51
Factors controlling alignment
Obligatory points
Traffic
Geometric design
Economics
Other considerations
Additional care in hill roads
Stability
Drainage
Geometric standards of hill roads
Resisting length
51

## Slide 52
Factors controlling alignment cont...
Obligatory points
Obligatory points through which alignment is to pass
Examples:-bridge site, intermediate town , Mountain pass etc…
Obligatory points through which alignment should not pass.
Examples:-religious places, costly structure, unsuitable land etc…
Traffic
origin and destination survey should be carried out in the area and the desire lines be drawn showing the trend of traffic flow.
New road to be aligned should keep in view the desired lines, traffic flow patterns and future trends.
52

## Slide 53
Geometric design
Design factors such as gradient ,radius of curve and sight distance also govern the final alignment of the highway.
Gradient should be flat and less than the ruling gradient or design gradient.
Avoid sudden changes in sight distance, especially near crossings
Avoid sharp horizontal curves
Avoid road intersections near bend
Economy
Alignment finalised based on total cost including initial cost, maintenance cost and vehicle operation cost.
Other consideration
Drainage consideration, political consideration
Surface water level, high flood level
Environmental consideration
53

## Slide 54
Topographical control points
The alignment, where possible should avoid passing through
  Marshy and low lying land with poor drainage
  Flood prone areas
  Unstable hilly features
Materials and constructional features
  Deep cutting should be avoided
  Earth work is to be balanced; quantities for filling and excavation
  Alignment should preferably be through better soil area to minimize pavement thickness
  Location may be near sources of embankment and pavement materials
54

## Slide 55
stability
A common problem in hilly roads is land sliding
The cutting and filling of the earth to construct the roads on hilly sides causes steepening of existing slope and affect its stability.
Drainage
Avoid the cross drainage structure
The number of cross drainage structure should be minimum.
Geometric standard of hilly road
Gradient, curve and speed
Sight distance, radius of curve
Resisting length
The total work to be done to move the loads along the route taking horizontal length, the actual difference in level between two stations and the sum of the ineffective rise and fall in excess of floating gradient. Should kept as low as possible.
55

## Slide 56
Before a highway alignment is finalised in highway project, the engineering survey are to be carried out. The various stages of engineering surveys are
Map study (Provisional alignment Identification)
Reconnaissance survey
Preliminary survey
Final location and detailed surveys
Engineering Surveys for Highway locations
56

## Slide 57
Drawing and Report
Key map
Index map
Preliminary survey plans
Detailed plan and longitudinal section
Detailed cross section
Land acquisition plans
Drawings of cross drainage and other retaining
structures
Drawings of road intersections
Land plans showing quarries etc
57

## Slide 58
New highway project
Map study
Reconnaissance survey
Preliminary survey
Location of final alignment
Detailed survey
Material survey
Geometric and structural design
Earth work
Pavement construction
Construction controls
58

## Slide 59
Two lane two-way road
carriageway
59

## Slide 60
shoulder
Footpath
Cycle track
60

## Slide 61
unTreated shoulder
Treated
shoulder
61

## Slide 62
Median/
separator
4-lane divided carriage way or dual carriage way
62

## Slide 63
kerb
63

## Slide 64
Frontage
road
64

## Slide 65
65

## Slide 66
Guard rails
66

## Slide 67
Horizontal
curve
67

## Slide 68
Rigid Pavement
68

## Slide 69
Flexible pavement
Rigid pavement
69

## Slide 70
FLEXIBLE PAVEMENT
RIGID PAVEMENT
70

## Slide 71
71
Thank You