## Slide 1
HIGH PERFORMANCE CONCRETE
Mr. Y. S. Lanjewar
Assistant Professor
St. VINCENT PALLOTTI COLLEGE OF ENGINEERING &
TECHNOLOGY,NAGPUR
DEPARTMENT OF CIVIL ENGINEERING

## Slide 2
At the end of this session, you will be able to understand
The concept of High performance Concrete (HPC)
Material Requirement for HPC
Application of HPC
Learning Outcomes

## Slide 3: Content
Introduction.
What is High Performance Concrete. ?
Components/Ingredients of HPC.
Methods for achieving High Performance
Characteristic of HPC.
Advantages.
Disadvantages.
Application.
Case Study.

## Slide 4
INTRODUCTION
Concrete is the most widely used construction material in India with annual consumption exceeding 100 million cubic meters.
High performance concrete is a concrete in which certain characteristics are developed for a particular application and environment, so that it will give excellent performance in the structure in which it will be placed.
A high-strength concrete is always a high performance concrete, but a high-performance concrete is not always a high-strength concrete.

## Slide 5
What is High Performance Concrete ?
According to Paul Zia
HPC is a concrete, which meets special performance, and uniformity requirements that cannot be always achieved by using only the conventional materials and normal mixing, placing, and curing practices.

## Slide 6
According to Civil Engineering Research Foundation (CERP)
HPC is a concrete in which some or all of the following properties have been enhanced.
Ease of placement
Long term mechanical properties
Early age strength
Toughness

## Slide 7
Components/Ingredients The main ingredients of HPC are as follows
Cement
Fine aggregate
Coarse aggregate
Water
Mineral admixtures (fine filler and/or pozzolonic supplementary cementitious materials)
Chemical admixtures (plasticizers, superplasticizers, retarders, airentraining agents)

## Slide 8
Methods for achieving High Performance
Better durability performance has been achieved by using high- strength, low w/c ratio concrete.
Two approaches to achieve durability through different techniques are as follows
1. Reducing the capillary pore system such that no fluid movement can occur is the first approach. This is very difficult to realize and all concrete will have some interconnected pores.

## Slide 9
2. Creating chemically active binding sites which prevent transport of aggressive ions such as chlorides is the second more effective method

## Slide 10
Characteristics of High performance concrete
Concrete may be regarded as high performance for several different reasons:
Very low porosity through a tight and refined pore structure of the cement paste.
Very low permeability of the concrete
High resistance to chemical attack.
Low heat of hydration

## Slide 11
High early strength and continued strength development
Low water binder ratio
Low bleeding and plastic shrinkage

## Slide 12
Advantages
Speed Of Construction
Economical Material In terms Of Time And Money
Higher Seismic Resistance
Improved Durability
Abrasion Resistance
High Tensile Strength
Reduced Maintenance Cost
Service life more than 100 years

## Slide 13
Disadvantages
An Extended Quality Control
Cost
Special Constituents
Manufactured And Placed carefully

## Slide 14
Application
In Pavements
High Performance concrete is being increasingly used for highway pavements due to the potential economic benefits
Fast track concrete paving (FTCP) technology can be used for complete pavement reconstruction.

## Slide 15
In Bridges
HPC is being extensively used now for the fabrication of precast pylons, piers, and girders of many long span bridges in the world, For Example The Normandie Bridge in France (1993),
Concrete structures are preferable for railway bridges to eliminate noise and vibration problems and minimize the maintenance cost.
Fast track concrete paving (FTCP) technology can be used for complete pavement reconstruction.

## Slide 16
Application
In High-rise Buildings
The reasons for using the high strength concrete in the area of high-rise buildings are to reduce the dead load, the deflection, the vibration and the noise, and the maintenance cost.
Miscellaneous Applications
Fiber reinforced concrete has been used with and without conventional reinforcement in many field applications. These include bridge deck overlays, floor slabs, pavements and pavement overlays, refractories, hydraulic structures, thin shells, rock slope stabilization, mine tunnel linings and many precast products.